## Slide 1: Keeping Things Stable
How Controllers Tackle Complexity in Modern Physics
EXERCISE

## Slide 2: Overview
Introduction
Exercises
  1: PID
  2: LQR
Competition
Discussion

## Slide 3: Inverted pendulum
Actor ()
Sensor ()
Source: STMicroelectronics, STSW-EDUKIT01 (graphic on product page); accessed 16 Feb 2026.

## Slide 4: Exercise procedure
Work in teams of 2 (max 3) people
  Ideally: One is good in python, other one good in math.
Python notebook with a simulation of the inverted pendulum
  It contains 2 examples to click through and 2 exercises (PID and LQR)
  Just change code where #TODO is written
  Write down your best parameters for the competition!
GIT: https://github.com/alboeh/iCSC-2026-exercise.git

## Slide 5: Run the notebook
Login to SWAN: https://swan.cern.ch
  Non-cern users can get licenses from the CSC team
Start session
  New JupyterLab interface
  LCG curated stack, General purpose Software stack (108)
  Check “Use python packages installed on CERNBox”
  Use 4 CPU and 16 GB RAM
Click left on Git and clone exercise rep, include submodules and download rep, ignore error msg
Open exercises/InvPendulum.ipynb (not solution!)
  Use “show_animation” function wisely, its time consuming
Alternatively: Clone on your local machine, may be faster!

## Slide 6: Exercise 1: PID control

## Slide 7: Solutions Exercise 1 (PID)
There is not the “optimal” solution!
I found this PD okayish, which was and
This is the reason we want a State-space controller!

## Slide 8: Exercise 2: State-Space control

## Slide 9: Solutions Exercise 2 (LQR)
Lets have a look into the code together!

## Slide 10: Solutions Exercise 2 (LQR)
Everything smooth and stable now :)
I used
Q=(100, 1, 1000, 1)
And R=100

## Slide 11: Solutions Exercise 3 (step)
We just want to change phi. Nevertheless, the controller did something „wrong“ here on purpose by counteracting the motion!
A PID would never do that, because it is „stupid“. A LQR instead knows the system and is smarter!

## Slide 12: Solutions BONUS Exercise (LQI)
I used
Q=(100, 1, 1000, 1, 50000)
And R=100

## Slide 13: Competition

## Slide 14: The rules
Taking your LQR / LQI values!
Sequence of positions (0°  30°  -30°  0°, each for 5s)
Score = RMS(theta) + 1/10 * RMS(phi)
  RMS only from 5 seconds on, so you have initially time to stabilize!
1x try per group during the exercise, 1 final shot!
Lowest score is the winner! 

## Slide 15: The rules
Example
Lowest score is the winner! 

## Slide 16: Discussions

## Slide 17: Some questions…
Is a PID or LQR better for the inverted pendulum?
Which PID parameters and method you used? Which LQR weights?
How much of a difference you noticed between the simulated and the real pendulum?
Has the winning team got the “best” controller? Or were they lucky?

## Slide 18: … and some answers
Is a PID or LQR better for the inverted pendulum?
  It depends in general! But here the LQR was better, it counteracted the motion
Which PID parameters and method you used? Which LQR weights?
  ZN is hard if system is intrinsically non-linear. PD worked best for me. I weighted theta and phi the strongest, the velocities not that much.
How much of a difference you noticed between the simulated and the real pendulum?
  Even though the simulation ran on non-linearized equations, it is nearly impossible to simulate it perfectly. Many things were not fully described, like the stepper dynamics, friction models, and much more!
Has the winning team got the “best” controller? Or were they just lucky?
  There is not something like a “best” controller. Maybe they build the “best” in keeping the pole vertically, but this is always a trade-off. E. g. maybe other groups had better results in terms of robustness (so more stable for big disturbances)

## Slide 19: Take-aways
PID
  No description of system necessary, fast solution
  Only one output can be controlled (without further ado)
  SISSO systems
State-Space
  Modelling necessary
  Therefore full state controllable
YES: Most of the life of a control engineer is to understand the system and find a good linearization, not the control itself 

## Slide 20: Thank you!
https://www.youtube.com/watch?v=Rh7JuL3PRSY
Full git project (with all plots, examples, etc) https://github.com/alboeh/iCSC-2026-full.git